## Slide 1
StrideTracked
A step towards security

## Slide 2
What is StrideTracked?
The Evolution of
Biometric Identification
Notes: - We all produce vibrations on the ground while walking
-We all have a different walking style that is given by our height/proportions, our weight and type of footwear
-The produced vibrations can be captured by accelerometers and gyroscopes placed anywhere in a room
-The software we developed leverages this concept to learn the walking style of a person and enables it to detect and identify the corresponding individual

## Slide 3
What is StrideTracked?
The Evolution of
Biometric Identification
Notes: - We all produce vibrations on the ground while walking
-We all have a different walking style that is given by our height/proportions, our weight and type of footwear
-The produced vibrations can be captured by accelerometers and gyroscopes placed anywhere in a room
-The software we developed leverages this concept to learn the walking style of a person and enables it to detect and identify the corresponding individual

## Slide 4
Product focus
UNOBTRUSIVE
Few small and power efficient devices positioned around the house can grant full coverage.
Notes: The 3 Key Product Focus:
1. Unobtrusive: With "StrideTracked," we have eliminated the need for intrusive/invasive or complex sensors(such as cameras, microphones,..). Just a few strategically positioned devices in your home can provide full coverage.
2. Secure: Data security is at the core of our product. No private data is shared outside of your own home. We have built a system that ensures no compromising information is recorded or transmitted. Your privacy is safe with "StrideTracked."
3. Intelligent:
since it can process the data locally, recognize the people or detect if there is any intruder.
We designed "StrideTracked" to be easily integrated with other system(for example we can integrate it with the home security system in order to warn the owner of any unidentified individual in the house.).
The first setup & configuration is also very easy, it just requires few minutes.
furthermore: The system can always remain on:
because is also equipped with a Sleep Mode. so It automatically deactivates when no movement is detected for long periods, and starts immediately recognizing individuals as soon as a vibration is sensed.

## Slide 5
Product focus
UNOBTRUSIVE
Few small and power efficient devices positioned around the house can grant full coverage.
SECURE
No private data gets shared outside of your own home.
No compromising data gets recorded.
Notes: The 3 Key Product Focus:
1. Unobtrusive: With "StrideTracked," we have eliminated the need for intrusive/invasive or complex sensors(such as cameras, microphones,..). Just a few strategically positioned devices in your home can provide full coverage.
2. Secure: Data security is at the core of our product. No private data is shared outside of your own home. We have built a system that ensures no compromising information is recorded or transmitted. Your privacy is safe with "StrideTracked."
3. Intelligent:
since it can process the data locally, recognize the people or detect if there is any intruder.
We designed "StrideTracked" to be easily integrated with other system(for example we can integrate it with the home security system in order to warn the owner of any unidentified individual in the house.).
The first setup&configuration is also very easy, it just requires few minutes.
furthermore: The system can always remain on:
because is also equipped with a Sleep Mode. so It automatically deactivates when no movement is detected for long periods, and starts immediately recognizing individuals as soon as a vibration is sensed.

## Slide 6
Product focus
UNOBTRUSIVE
Few small and power efficient devices positioned around the house can grant full coverage.
SECURE
No private data gets shared outside of your own home.
No compromising data gets recorded.
INTELLIGENT
Fast and easy first integration.
No need to get turned on/off
Personalized identification based on a custom model.
Notes: The 3 Key Product Focus:
1. Unobtrusive: With "StrideTracked," we have eliminated the need for intrusive/invasive or complex sensors(such as cameras, microphones,..). Just a few strategically positioned devices in your home can provide full coverage.
2. Secure: Data security is at the core of our product. No private data is shared outside of your own home. We have built a system that ensures no compromising information is recorded or transmitted. Your privacy is safe with "StrideTracked."
3. Intelligent:
since it can process the data locally, recognize the people or detect if there is any intruder.
We designed "StrideTracked" to be easily integrated with other system(for example we can integrate it with the home security system in order to warn the owner of any unidentified individual in the house.).
The first setup&configuration is also very easy, it just requires few minutes.
furthermore: The system can always remain on:
because is also equipped with a Sleep Mode. so It automatically deactivates when no movement is detected for long periods, and starts immediately recognizing individuals as soon as a vibration is sensed.

## Slide 7
Owner's life could depend on the effectiveness and efficacy of the device
Accuracy & reliability
New people entering the house should be warned that they are being recorded
Informed consent
The recorded data is different from common security systems and inherently more secure
Less sensitive data
Ethical perspective
02.
03.
01.
Notes: Informed Consent: Consent is a crucial aspect of ethical data collection and surveillance. Individuals should be fully informed about the purpose, scope, and potential risks of the device's operation within their home. They should have the right to choose whether they want to participate or opt out without facing any negative consequences.
Less sensitive data: The kind of data which our device is using is way less private than other types of data which other monitoring systems capable of identify individuals use. This from the ethical perspective means that users might be more incline to use our device knowing that their privacy is less at risk but can still get a rewarding user experience.
Accuracy and reliability: While data security may not be an immediate concern, trust and reliability are still important ethical considerations. Individuals need to trust that the device will accurately recognize their identity and protect their privacy. The technology should be reliable and not prone to errors or false identifications, which could lead to unintended consequences.
Function Creep: Even if the initial purpose of the device is identity recognition, there is a risk of function creep, where the device's capabilities or usage may expand over time without the explicit consent or knowledge of the individuals being monitored. Ethical considerations should be given to ensuring that the device's usage remains within the agreed-upon scope and that any changes or additional functionalities are communicated transparently and with the individual's consent.
Autonomy and Consent: While local data processing may alleviate some privacy concerns, individuals still have the right to autonomy and control over their personal information. Consent should be obtained before implementing the device, and individuals should have the ability to withdraw their consent at any time. They should also have access to their data and the ability to delete or modify it if desired.

## Slide 8
Marketing perspective
A new forward-thinking device for your home which provides
convenience, privacy, and peace of mind
Collaborating with security companies the device could be seamlessly integrated with existing security systems
Security
We can achieve an higher degree of automation by recognizing the people walking inside a room without any need to speak or being recorded.
Home automation

## Slide 9
A boom in the use of smart
low power devices is expected
in years to come.
Future-Proof Technology
Our low power device and sensors can perform the same task that cameras perform with a huge waste of resources.
Energy Efficiency
We bring innovation
in a stale field
Combining cutting-edge biometric evaluation with local data processing we ensure uncompromised privacy. With a focus on personalized settings, each user benefits from a tailored home entry experience, eliminating the hassles of manual authentication.
The project is open source so any new user can tailor his experience to suit his needs.
Customizability

## Slide 10
Faced challenges
1
IMU precision
People
Time
Data gathering
Notes: The IMU standard Arduino library does not permit to change the refresh rate of the sensor to values different from 100Hz thus we had to find and fix a user made library that enables way higher customizability.
No publicly available dataset of steps recorded from an external device(with respect to the used) so we had to collect our own requiring lots of time and people

## Slide 11
Faced challenges
1
IMU precision
People
Time
Data gathering
2
Normalization
Feature reduction
Data handling
Notes: We had to try different types of normalizations and feature reduction techniques to achieve acceptable results from the algorithms we used

## Slide 12
Faced challenges
1
IMU precision
People
Time
Data gathering
2
3
Normalization
Feature reduction
Size
Limited layer types
Output
Data handling
CNN Tuning
Notes: The size of the CNN was a big concern since the memory of the Arduino is very limited. Also, the types of layers present in the TensorFlow Lite for micro are fewer with respect to the ones present in the full fledge TensorFlow library so big limitations were posed when deciding the network topology.
The output dimension was also a concern since the output of the network if used as a feature extractor would need to have a good dimensionality for the algorithm of choice

## Slide 13
Faced challenges
1
IMU precision
People
Time
Data gathering
Bias removal
2
3
Normalization
Feature reduction
Size
Limited layer types
Output
Data handling
CNN Tuning
Gravity
Signal power
Surface
Augmentation
4
Notes: When we started training the network with the first samples we noticed very high accuracy but this soon raised some doubts since we noticed that when passed on device the network was giving completely random results making us question the presence of a bias in the data. In fact we found that the position and orientation of the device in conjunction with the gravity direction and surface amplification of the vibrations could uniquely identify each recording. This problem was resolved by creating and applying different augmentations to the dataset

## Slide 14
Faced challenges
1
4
IMU precision
People
Time
Gravity
Signal power
Surface
Augmentation
Data gathering
Bias removal
2
3
5
Normalization
Feature reduction
Size
Limited layer types
Output
SVM
Random Forest
KNN
Data handling
CNN Tuning
On-device Learning
Notes: Different algorithms for on device learning were used but just the KNN was trainable on device with already existing libraries

## Slide 15
more than 10 different surfaces
200+ minutes
238 Hz
9 different people
+ noise class
IMU
refresh-rate
Data Gathering
We collected step data from 9 different individuals by placing the Arduino on various surfaces. Additionally, we incorporated background noise measurements in the absence of any person.
Francesco
Riccardo
Elia
Background noise
Mara
Annick
Valentina
Elisa
Ludovica
Francesca
2.15 seconds per sample
5375 samples
Accelerometer
Gyroscope
Down to 5 Hz in sleep mode
Notes: We collected data from background noise and from 9 different people, using the accelerometer and the gyroscope.
we also placed the board on different surfaces and we record strides with different footwear. and then with this dataset we trained the CNN.
the sampling rate was 238 Hz, for a total of around 5thousands samples (2.15 s/sample, that is the time of a stride)

## Slide 16
Java programming language we used in combination with the Arduino IDE and board to read sensor data and save it in useful formats while keeping an eye on the sensors waveforms
We decided to use the combination of the two sensors mounted on the IMU since different surfaces react differently to vibrations generating different movement patters on different axis
Processing
Accelerometer & gyro
Data Gathering
Notes: Here we take out the Arduino and we show how the gathering process was performed.
Using arduino we sent via serial the data
Using processing we visualize and save the recorded data in .csv with labels

## Slide 17
83 378
85 KB
Parameters
Convolutional Neural Network Topology
Memory occupation
  window size of 512 for 6 channels
  30% overlap
  No overlap on device
Windows & Overlapping
Notes: We first implemented a network with an input of 512 samples for each of the 6 channels and used big filters also thanks to the presence of a fire module. For the training of the network we implied the use of a 30% window overlap which was not possible to be performed on device due to the sequential nature of the Arduino code.

## Slide 18
Convolutional Neural Network Topology
83 378
87 KB
Parameters
Memory occupation
  Min-Max and Std normalization
  Random vector rotation, constant scaling, noise addition, time shift
  Class balancing
Normalization & Augmentation
Notes: We then introduced both normalizations and augmentations. We used the Min-Max normalization since the type of data that the sensor returns as is a 16 bit integer. We then went on by using different types of augmentations. The random vector rotation simulates a random rotation in the 3d space of the Arduino sensor by treating the 3 channels of each sensor as a 3d vector that gets rotated in space by the use of a rotation matrix. The constant scaling simply multiplies the signal by a random value to simulate a change in signal power. The noise addition is simply a gaussian noise addition to the signal and the time shift which by using a cyclical buffer shifts the signal in time by a random value.
Also class balancing with the mentioned augmentations was performed to balance the high number of background noise samples.

## Slide 19
99418
107 KB
Parameters
The fast Fourier transform is performed and only the magnitude of the signal is kept.
Noise is then added and a curve scaling is applied randomly
FFT introduced
Convolutional Neural Network Topology
Memory occupation
Notes: We introduced the FFT transform as the feature reduction step. From the FFT only the magnitude of the signal is kept thus enabling us to half the neural network input size. This change made us completely rebuild the network topology since the fire module was not achieving such great accuracy results.
To the FFT signal some simple augmentations are added such as random noise addition and random curve scaling (which performs a scaling of the obtained frequency with respect to a simple smooth curve in the [0.8-1.2] range) to further increase the dataset size

## Slide 20
Convolutional Neural Network Topology
98138
106 KB
Parameters
SVM and Random Forest are constrained to not be trained locally and achieved low accuracy. The KNN can be directly trained on device and achieved way higher accuracy
SVM - Random Forest - KNN
Memory occupation
Notes: To be able to perform the on device learning we had to remove the last layer of the CNN and use the second to last layer as a feature vector for the three machine learning algorithms that we tried. Both SVM and Random Forest did not achieve good results on testing and were both not present in already built Arduino libraries. We thus decided for the KNN since it achieved the best results and had the possibility to be trained locally

## Slide 21
Final Results
91.34 %
CNN test accuracy

## Slide 22
87.15 %
Quantized CNN
test accuracy
Final Results
91.34 %
CNN test accuracy

## Slide 23
94.49 %
87.15 %
Quantized CNN
test accuracy
Quantized CNN &
KNN test accuracy
Final Results
91.34 %
CNN test accuracy
Notes: the test accuracy is not representative of the real world accuracy

## Slide 24
DEMO TIME!
The Demo Effect

## Slide 26
Thank
you!
Notes: Riccardo Bravin
Francesco Caserta